## Slide 1: Parameter Conversion between NSI and MBIRCONE
0
04/09/2025

## Slide 2: NSI parameters
The NSI parameters includes the following:
    ; ; ; ; ; ; ; ; ; ; and
Assumed definition of NSI parameters:
    : 3D real-valued unit vector in direction of rotational axis pointing down
    : 3D real-valued unit vector perpendicular to the detector plane pointing from source to detector
    : 3D real-valued unit vector in direction parallel to detector rows pointing from left to right
    : 3D real-valued vector from origin to source location in mm
    : 3D real-valued vector from origin to center of pixel on first row and column of detector
    : 2D real-valued vector defining spacing between rows and columns in mm, respectively
    : integer number of detector channels
    : integer number of detector channels
    : Boolean variable (true/false) that determines if the rotation direction is clockwise viewed from the top.
    number: integer number that determines number of projection angles.
    angleStep: float number that determines the angle step size in degrees between adjacent projection measurements.

## Slide 3: Graphic illustration of NSI parameters
NSI parameters:
    : 3D real-valued unit vector in direction of rotational axis pointing down
    : 3D real-valued unit vector perpendicular to the detector plan pointing from source to detector
    : 3D real-valued unit vector in direction parallel to detector rows pointing from left to right
    : 3D real-valued vector from origin to source location in mm
    : 3D real-valued vector from origin to center of pixel on first row and column of detector
    : 2D real-valued vector defining spacing between rows and columns in mm, respectively
    : integer number of detector channels
    : integer number of detector rows
    : Boolean variable (true/false) that determines if the rotation direction is clockwise viewed from the top.
    : integer number that determines number of projection angles.
    : float number that determines the angle step size in degrees between adjacent projection measurements.
source
row index
Rotation axis
=axis
normal
horizontal
reference
center of detector
channel index
Origin =
Assumed to fall along the rotation axis
coordinates system

## Slide 4: Source-Detector Parameters
Inputs:
  : 3D real-valued unit vector in direction of rotational axis pointing down
  normal: 3D unit vector perpendicular to the detector plane pointing from source to detector
  : 3D real-valued unit vector in direction parallel to detector rows pointing from left to right
  source: 3D vector from origin to source location
  reference: 3D vector from origin to center of (0,0) detector pixel
Output:
  : float number specifying the distance between the X-ray source and the detector panel in units of ALU.
  magnification: float number specifying the magnification of the cone-beam geometry
  clockwise rotation of each view that is required to correct svmbir data
Pseudocode:
calc_source_detector_params( , , , ):
  //Make sure is normalized
  //Calculate
  //Ignores out-of-plane tilt of the rotation axis
  //Project the rotation axis onto the detector plane.
  //Normalize the result.
  //Calculate required rotation angle for view correction.
  Return(, , )
Detector panel
channel index
row index

## Slide 5: Detector row, channel parameters
Inputs:
  : 3D real-valued unit vector in direction of rotational axis pointing down
  normal: 3D unit vector perpendicular to the detector plane pointing from source to detector
  : 3D real-valued unit vector in direction parallel to detector rows pointing from left to right
  source: 3D vector from origin to source location
  reference: 3D vector from origin to center of (0,0) detector pixel
  : 2D real-valued vector defining spacing between rows and columns in mm, respectively
  : integer number of detector channels
  : integer number of detector rows
Outputs:
    : float number specifying the distance in ALU from center of detector to the source-detector line along a row.
    : float number specifying the distance in ALU from center of detector to the source-detector line along a column.
    rotation_offset: Scalar value describing the distance in ALU from source-detector line to axis of rotation.
    : float number specifying the detector channel spacing in ALU.
    : float number specifying the detector row spacing in ALU.
Pseudocode:
calc_row_channel_params(, , , , , , , , ):
//Make sure is normalized
; //Make sure is perpendicular to and normal
//Make sure is normalized
Return(, , , , )

## Slide 6: Geometric Interpretation of calc_row_channel_params
Rotation axis
X-ray
source
Center of detector
center of detector pixel
row index
channel index
Origin =
Assumed to fall along the rotation axis
Source-detector line

## Slide 7: Recap: conversion algorithm between NSI and MBIR params
Rotation axis
X-ray
source
Center of detector
center of detector pixel
row index
channel index
Origin =
Assumed to fall along the rotation axis
Source-detector line
calc_row_channel_params(, , , , , , , , ):
//Make sure is normalized
; //Make sure is perpendicular to and normal
//Make sure is normalized
Return(, , , , )
calc_source_detector_params( , , , ):
  //Make sure is normalized
  //Calculate
  //Ignores out-of-plane tilt of the rotation axis
  //Project the rotation axis onto the detector plane.
  //Normalize the result.
  //Calculate required rotation angle for view correction.
  Return(, , )

## Slide 8: Issue: location of (0,0) detector pixel is incorrect
Issue: our interpretation of the NSI metadata entry “reference” is incorrect.
    Our interpretation: 3D real-valued vector from origin to center of (0,0) detector pixel
    In reality: <reference> refers to a “virtual” detector pixel that is one pixel shifted from the physical location of (0,0) detector pixel.
row index
Rotation axis
center of detector pixel
channel index
Origin =
Assumed to fall along the rotation axis
coordinates system
Source
“virtual” detector pixel

## Slide 9: What is the “virtual” detector pixel?
NSI reconstruction process:
  multiple reconstructions are performed by shifting the coordinate of (0,0) detector pixel left/right to a virtual location.
  Technician visually inspects the recon results and picks the best one.
  The “virtual” detector pixel is the shifted (0,0) detector pixel corresponding to the best results.
The calculation of MBIR params should use the physical location of (0,0) detector pixel.
row index
Rotation axis
physical location of detector pixel
channel index
Origin =
Assumed to fall along the rotation axis
coordinates system
Source
“virtual” detector pixel

## Slide 10
Experiment: Compare recon quality with and without the correction of (0,0) detector pixel
Goal: Compare the recon quality with MBIR parameters calculated with and respectively.
  : vector from origin to the “virtual” detector pixel.
  : vector from origin to the “true” detector pixel.
Criteria:
  Expect higher image resolution with the correct approach.
  Expect less structural noise in sino error with the correct approach.
Datasets:
  MAR phantom, vertical scan
  MAR phantom, horizontal scan
  Reservoir scan
Experiment details:
  Half of sino views are used.
  Only reconstructed the central slices.
Results:
  In all cases the recon resolution using the corrected pixel location () is better with sharper edges.
  The sinogram error using the corrected pixel location () have less structural noise.
calc_row_channel_params(, , , , , , , , ):
//Make sure is normalized
; //Make sure is perpendicular to and normal
//Make sure is normalized
Return(, , , , )

## Slide 11
: sinogram view
Result comparison, MAR vertical
: sino error with (corrected)
: sino error with (uncorrected)
Recon with (corrected)
Recon with (uncorrected)

## Slide 12
: sinogram view
Result comparison, MAR horizontal
Recon with (corrected)
Recon with (uncorrected)
: sino error with (corrected)
: sino error with (uncorrected)

## Slide 13
: sinogram view
Result comparison, Reservoir
: sino error with (corrected)
: sino error with (uncorrected)
Recon with (corrected)
Recon with (uncorrected)

## Slide 14
Experiment: Verification of MBIR parameter calculation
Goal: Verify that the MBIR parameters calculated from NSI metadata is correct.
Recon to compare:
  Recon with MBIR calculated from NSI parameters
  Best recon results found with grid search strategy
    Fix and
    Perform grid search on the channel offset:
      , where .
    Previously: best channel offset:
Criteria:
  End-to-end: Expect image quality (1) (2)
  Look at the MBIR parameters and make sure they physically makes sense.
Experiment details:
  Dataset: MAR vertical dataset.
  Half of sino views are used.
  Only reconstructed the central slices.
Results:
  Recon quality with the calculated MBIR params is marginally better than the best recon quality found with grid-search.
  MBIR parameters physically make sense.
calc_row_channel_params(, , , , , , , , ):
//Make sure is normalized
; //Make sure is perpendicular to and normal
//Make sure is normalized
Return(, , , , )

## Slide 15
: sinogram view
Result quality comparison, MAR vertical
: sino error (calculated params)
: sino error (grid search)
Recon (calculated params)
Recon (grid search)

## Slide 16
MBIR parameter: rotation offset
Rotation axis
X-ray
source
Center of detector
row index
channel index
Origin =
Source-detector line
coordinates system
Goal: check that the sign and magnitude of makes sense.
Inputs (NSI metadata)
Calculated rotation offset:
Check sign: since the origin falls on the right side of the source-detector line, should be positive.
Check magnitude:
calc_row_channel_params(, , , , , , , , ):
//Make sure is normalized
; //Make sure is perpendicular to and normal
//Make sure is normalized
Return(, , , , )